## Slide 1: Arduino Workshop #8
Interfacing with liquid crystal displays
Notes: 24 - Arduino Uno
24 - USB cables
24 - Speakers
48 - pushbuttons
24 - Small DC fan
24 - 16x24 character LCD
48 - 4.7 ㏀ resistor
48 - 10 ㏀ resistor
24 - 150 Ω resistor
24 - 10 ㏀ POT
24 - TC74A0-0.5V I2C Temperature sensor
24 - jumper wire sets
24 - breadboards

## Slide 2: PowerPoint and Code
Github.com/EELabMan
Go To Repositories and find Arduino 8 LCD

## Slide 3: Setting up the LCD
We will be using pre soldered 16x2 LCDS
  If after this you choose to purchase a LCD for a project, know that some come w/o the headers soldered on and may have dirrecent pinouts.
  16x2 refers to the number of columns and rows the LCD displays
    16 columns
    2 rows

## Slide 4: Looking at the pin out

## Slide 5: Breaking down the pins
Pin 3 (contrast) - controls how dark the display is. It connects to the center pin of our POT
Pin 4 (RS) - sets the LCD to command or character mode
  Based on its state the LCD is either interpreting data as a command or a character
Pin 5 (RW) - tied to ground
  indicating we will only ever be writing to the LCD not reading from it
Pin 6 (EN) - used to tell the LCD when data is ready
Pins 7 to 14 - used to transmitting data
  Usually labeled D0 to D7 (in order)
  pins 7 to 10 (D0 - D3) will be unused by us
Pin 15 and 16 - run the back light
  Connect them to 5v (pin 15) and ground (pin 16) with a current limiting resistor as needed

## Slide 6: Connecting to the arduino
You can connect the communication pins on the LCD to any I/O pins on the arduino
To be consistent with the group we will use
LCD Pin | Arduino Pin
RS | Pin 2
EN | Pin 3
D4 | Pin 4
D5 | Pin 5
D6 | Pin 6
D7 | Pin 7

## Slide 7: Lets wire up the LCD

## Slide 8: Using the LiquidCrystal Library
The Arduino IDE includes the LiquidCrystal library
It includes simplified functions to
Blinking the cursor
Automatically scrolling text
Creating custom characters
Changing direction of printing
Many other useful additions and functions
You can find description of the library function as well as examples of use at
http://arduino.cc/en/Reference/LiquidCrystal

## Slide 9: Adding text to the display
The first thing we will be doing in order to learn the basic operation of the LCD is to add text and an incrementing number to the display
To initialise the LCD we use the following code
#include <LiquidCrystal.h>
  Initiallizes the liquid crystal library
LiquidCrystal lcd (2,3,4,5,6,7);
  This creates a liquid crystal obj named lcd and the arguments represent the pins connected (RS,EN,D4,D5,D6,D7 in that order)
lcd.begin(16,2)
  This sets the LCD display character size as a number of rows and col respectively
lcd.setCursor(0,1)
  This moves the cursor to a specific spot
    Columns and rows are indexed (0,0) in the top-left
lcd.Print(“We love EE”)
  This will print what ever characters you supply (as a char and that will fit in the dimensions of the LCD)

## Slide 10: Adding it all to a sketch
Download LCD_text.ino from github and upload it.
You should see your message with a counter increasing every second

## Slide 11: Creating Special Characters or Animations
If you want special characters, degrees sign, greek letters - the LiquidCrystal library supports the definition of custom Characters
To create a custom character
You will notice each character block is really made up of a 5x8 grid of pixels
You simply define the value of each of these pixels and send that information to the display

## Slide 12: Demonstration of this concept
We will make a series of characters that will fill the second row of the display with an animated progress bar
Each space is 5 pixels wide
  So there will be 5 custom characters
    1st column filled
    1st & 2nd col filled
    Etc.
We will use binary to encode the state of the pixel (1 is on 0 is off)

## Slide 13: Defining your special caharacters
Download LCD_progress_bar.ino from github and upload it.

## Slide 14: Building a personal thermostat

## Slide 15: Items we will use
A DC fan
  If you want to add some oomph you can wire it with a transistor and external voltage supply (like session 4 shows), but hooking it to the 5V pins will show it spins when it should
Two buttons with 10 ㏀ pull - down resistors
A speaker
  Connected to an I/O pin through a 150 Ω resistor and ground
  We will set the frequency in the program
I2C temperature sensor
  Hooked up exactly as we learned in lesson 8
    To preserve space we will place this in front of the LCD’s potentiometer

## Slide 16: It should be wired like this

## Slide 17: The custom characters

## Slide 18: We will utilize them and refresh the screen as shown

## Slide 19: Adjusting the set point with buttons

## Slide 20: Updating the LCD
This code
first runs the debounce() function for each button and then adjusts the set temp variable if one button is pressed
Updates the LCD and button states

## Slide 21: Adding audio warning and fan
Here we see
tone()
  Paired to a delay() and notone() command
Using a state variable we determine if the speaker has beeped
  And don't let it beep again until after the temp dips (and the state variable is reset)
When the fan turns on and indicator on the LCD changes

## Slide 22: Bring it all together
You should now have a fully functioning code (combining all the snippets from earlier to all work together to produce the desired result)
Once you load the code onto the arduino you no longer need to have it connected to a computer to run, you could take it and place it anywhere in the room to tell you the temperature (as long as you can connect it to a plug (or battery))

## Slide 23: The LCD should look similar to this

## Slide 24: Stay tuned
Arduino 9 will cover how to send and receive data using Bluetooth.
We’ll also connect to our smart phones and control some LED’s!